|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 9/3/13 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Soil Sampling Via Direct Push Drilling |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Severity | Probability | Score | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. |
| --- | --- | --- | --- | --- | --- |
| Drill Rig Arrival and Set-Up. | See “unloading/loading equipment” JSA |  |  |  |  |
| Drill Rig Inspection | Defective/damaged equipment | 2 | 2 | 4 | Inspection of equipment by qualified driller prior to use; replace or repair damaged items with manufacturer |
|  | Damaged Drive Assembly | 1 | 2 | 2 | Inspection of drive assembly by driller prior to use: cracks or damaged parts must be repaired or replaced. |
| Attach Casing Lengths | Back Strain | 2 | 2 | 4 | Minimize carrying distance as much as possible. |
|  | Crushed Foot | 3 | 1 | 3 | Steeltoe shoes/boots |
|  | Pinched/Lacerated Fingers | 2 | 3 | 6 | Communication between employees when moving/attaching casing sections; Wear leather gloves when handling sections. Keep hands clear/out of pinch points. |
| Ground Intrusion | Laceration injury from flying debris due to percussion caused by drilling method. | 2 | 2 | 4 | Clear the area of obstructions and communicate with all parties that drilling is beginning. Do not exceed manufacturers recommended rate of speed, force, etc. Penetrate the ground slowly with hands on the controls for the first foot of soil. Protective lenses are recommended. |
|  | Noise | 2 | 1 | 2 | Use hearing protection. |
|  | Overhead Falling Hazards | 2 | 2 | 4 | Use Hard Hat; remove overhead hazards promptly |
| Retrieve sampling tooling and open acetate liner. | Pinch points created by Geoprobe connection points with casing. | 2 | 2 | 4 | Wait until driller comes to complete stop with casing retrieval before helper may assist in dethreading casing. Practice safe lifting techniques when handling casing. |
| Should liners become jammed, the casing will be attached to the extruder to push liners out. | Muscle strain | 2 | 2 | 4 | When connecting to extruder two man crew should assist one another when attaching casing. |

# Text boxes

## Yes             No