|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 1/25/2013 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Number: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Loading and Unloading equipment in/near roadway |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Pre Mobilization Site Meeting | Auto/Public Traffic Non-Compliance to traffic laws | Plan drop zone before arriving at site. Drop off zone must be determined to comply with City ordinances and public law. | Site Supervisor, Driver |
| Loading and Unloading Equipment | Auto/Public Traffic | Delivery Vehicle must be equipped with proper warning lights. (flashers, strobe lights). | Driver |
|  |  | Personnel in the loading and unloading zone must wear proper PPE – safety vests. | Driver, Driller, Helper |
|  |  | Equipment being strapped or unstrapped on traffic side should have a spotter | Driver, Helper |
|  |  | Flaggers may be required for temporary lane closure. Traffic control signs or cones to be utilized warning drivers of activity in roadway. | Site Supervisor, Driller |
|  | Steel tracks causing property damage to asphalt | Use mats to protect ground | Driller, Helper |
|  | Overhead Utilities | Identify low hanging lines while loading and unloading equipment | Site Supervisor, Driller, Helper |
|  | Crush and pinch points | Wear leather gloves at all times | Driver, Driller, Helper |
|  |  | Keep feet clear of ramps and tracks | Driver, Driller, Helper |
|  |  | ALL EMPLOYEES TO BE ACCOUNTED FOR AND NOTIFIED BEFORE EQUIPMENT IS TO BE MOVED | Driver, Driller, Helper |

# Text boxes

## Yes             No