|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 4/24/13 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Moving track rig |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Make sure all equipment is secure on rig. | Lose equipment, Falling/struck by tooling | Ensure appropriate tie downs have secured equipment. All boxes are closed and latched so loss of tools or supplies occurs. Wear appropriate PPE: Hardhat, steel toe boots | Driller’s Helper |
| Determine path of access | Trip hazards: vegetation and uneven terrain Insect bite | Locate safe travel path with minimal obstructions to reduce risk of tripping. Watch foot placement. Use insect repellent. Communicate with others on crew to identify and avoid potentially hazardous areas | Driller/Driller’s Helper |
| Clear a path (if necessary) | Review chainsaw JSA before using | Wear appropriate PPE for Chainsaw Safety (chaps, face guard, leather work gloves, steel toe boots) | Driller/Driller’s Helper |
| Move drill rig | Struck by machine Rollover/tip over | Use verbal or non verbal communication with helper to ensure they stand safe distance from rig. Dependent upon terrain and access driller’s helper must be prepared to adjust their position around the rig. Driller should move up and down on slopes. Not side to side to avoid risk of rollover. | Driller’s Helper Driller |

# Text boxes

## Yes             No