|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 02/15/2013 |  | Job number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Using oxyacetylene gas outfit to heat and cut steel |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Clear the area for work | Slip and trip Fire Explosive environment | Remove trip hazards, clear area of debris and flammable material, oxyacetylene mixtures burn in excess of 6000 degrees F. | Shop foreman, mechanic, weldor, driller and helper, owners and sightseers |
| Secure gas bottles in upright position with valves in off position | Blunt force trauma Projected missile Explosion | Use proper cart and chain or strap bottles to cart or other sturdy object, transport bottles in vertical position, keep safety caps covering valves until bottles are secured | Operator |
| Use proper PPE | Eye damage from flash/splash Skin and hair burns | Dark goggles Long sleeves/pants and tight fitting cap or hat made of cotton or cotton/poly blends (NO nylon/spandex or technical clothing outerwear), heavy leather gloves | Operator and Helper |
| Use proper tip nozzle for work to be done | Eye damage from flash/splash Excessive heat | Dark goggles Rosebud or smaller tip for heating, no actuator handle Cutting tip has actuator handle for oxygen release | Operator |
| 5. Set working pressure on regulators | Gauge Failure | Stand to side away from regulators. Back off regulators to no resistance. Turn on valves SLOWLY, one- quarter turn only. Set working pressure on regulators SLOWLY. | Operator |
| Use correct psi setting for work being done | Excessive heat, splash Fire | Start with 5 psi for acetylene and 30 psi for oxygen for cutting, increase acetylene by 1-2 psi for thicker metals Rosebud heating tip= 14 psi acetylene, 15 psi oxygen | Operator |
| Work complete | Damage to facilities and equipment | Turn off valves on tanks first, then release pressure on gauges. Check for leaks, drain gas from hoses and rewrap | Operator and Helper |

# Text boxes

## Yes             No