|  | Activity Hazard Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 8/26/2012 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Well Development |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| MOBILIZATION TO SITE | DRIVING ACCIDENTS | ALL VEHICLES TO COMPLY WITH CONNELLY DRIVING SAFETY STANDARDS | DRILLER / CONSULTANT |
|  |  | VEHICLE TO BE FIT FOR PURPOSE AND WELL MAINTAINED. | DRILLER / CONSULTANT |
|  |  | LOADS TO BE SECURE AND NOT TO EXCEED VEHICLE SPECIFICATIONS OR LEGAL LIMTS. | DRILLER / CONSULTANT |
|  |  | DRIVER TO BE LICENCED, TRAINED AND MEDICALLY FIT | DRILLER / CONSULTANT |
|  |  | DRIVER TO BE RESTED AND ALERT | DRILLER / CONSULTANT |
|  |  | MOBILE PHONE OR TWO-WAY RADIO TURNED OFF WHILE DRIVING | DRILLER / CONSULTANT |
|  |  | PLAN YOUR ROUTE AHEAD OF TIME | DRILLER / CONSULTANT |
|  |  | DRIVER NOT BE UNDER THE INFLUENCE OF ALCOHOL, DRUGS OR MEDICATION THAT IMPAIRS ABILITY TO DRIVE VEHICLE. | DRILLER / CONSULTANT |
| SET UP WORK SITE | AUTO / PUBLIC TRAFFIC | NOTIFY ATTENDANT OR SITE MANAGER / OWNER OF WORK ACTIVITIES AND LOCATION. |  |
|  |  | WORK LOCATION TO BE BARRICADED OFF; VEHICLE AND PEDISTRIAN TRAFFIC MANAGEMENT PLAN AS REQUIRED | DRILLER / Consultant |
| SET UP WORK SITE (Cont’d) | AUTO / PUBLIC TRAFFIC (Cont’d) | HIGH VISIBLE CLOTHING, STEEL CAP BOOTS, LONG SLEEVES/PANTS/ HARD HAT / SAFETY GLASSES TO BE WORN AT ALL TIMES WHILE IN OPERATIONAL AREAS | DRILLER / Consultant |
|  |  | INSPECT AREA AROUND VEHICLE PRIOR TO PUTTING VEHICLE IN MOTION AND USE SPOTTER | DRILLER / CONSULTANT |
|  | UNEVEN OR UNSTABLE GROUND | Visually examine site prior to entry. Place timbers under outriggers to spread load. | Driller |
|  | UNEVEN OR UNSTABLE GROUND | Visually examine site prior to entry. Place timbers under outriggers to spread load. | Driller |
|  |  | electrical spotter to be employed when working within 3 – 6.4 m (10 TO 20 FEET) of OHE lines; power company permit also required | CONSULTANT |
|  | UNDERGROUND SERVICES | UNDERGROUND SERVICES TO BE LOCATED PRIOR TO BREAKING GROUND BY QUALIFIED SERVICE LOCATOR | CONSULTANT / SERVICE LOCATOR / DRILLER |
| WELL DEVELOPMENT | PRE-WORK INSPECTION | INSPECT ALL HAND TOOLS PRIOR TO USE. IF FAULTY OR INAPPROPRIATE, DO NOT USE UNTIL REPAIRED OR REPLACED | DRILLER |
|  |  | INSPECT AIR COMPRESSOR/DEVELOPMENT PUMP. CHECK FOR FAULTY WIRING, MAKE SURE COMPRESSOR FUEL TANK IS FULL | DRILLER |
|  |  | SET-UP ADEQUATE EXCLUSION ZONE – ONLY TRAINED, INDUCTED AND AUTHORIZED PERSONNEL WITHIN THIS AREA | DRILLER |
|  |  | WEAR APPROPRIATE PPE INCLUDING LEATHER GLOVES, STEEL CAPPED BOOTS, HARD HAT, AND SAFETY GLASSES. FULL LENGTH OVERALLS OR LONG SLEEVE SHIRT AND LONG PANTS - NO LOOSE CLOTHING, Fire retardent clothing (FRC) WHEN APPROPRIATE. | DRILLER |
|  |  | STOP WORK IF HAZARDOUS CONDITIONS IDENTIFIED (EXPLOSIVE ATMOSHPERE, O2 DEFICIENT OR ENRICHED ATMOSPHERE) – REASSESS AND TAKE THE NECESSARY PRECAUTIONS. | DRILLER / CONSULTANT |
|  | SLIP, TRIP & FALL | KEEP WORK AREA TIDY, STAY AWARE OF FOOTING AND DO NOT RUN | DRILLER / CONSULATANT |
|  | HEAT / COLD STRESS | TAKE REGULAR BREAKS ON HOT DAYS OR IF FEELING FAINT OR OVEREXERTED | DRILLER / CONSULATANT |
|  |  | CONSUME ADEQUATE FOOD / BEVERAGES (WATER / SPORTS DRINK) | DRILLER / CONSULATANT |
|  |  | IF POSSIBLE, ADJUST WORK SCHEDULE TO AVOID TEMPERATURE EXTREMES | DRILLER / CONSULATANT |
|  | BIOLOGICAL HAZARDS: INSECTS, SNAKES, WILDLIFE, VEGETATION | CAREFULLY INSPECT WORK AREA DURING SITE INSPECTION TO IDENTIFY HAZARDS | DRILLER / CONSULATANT |
|  |  | USE INSECT REPELLANT | DRILLER / CONSULATANT |
|  |  | OPEN ENCLOSURES SLOWLY | DRILLER / CONSULATANT |
|  |  | SURVEY SITE FOR PRESENCE OF BIOLOGICAL HAZARDS AND MAINTAIN SAFE DISTANCE | DRILLER / CONSULATANT |
|  |  | WEAR APPROPRIATE PPE INCLUDING LEATHER GLOVES, LONG SLEEVES AND PANTS AND SNAKE CHAPS AS REQUIRED | DRILLER / CONSULATANT |
|  | UV EXPOSURE | WEAR CORRECT PPE (NECK TO TOE CLOTHING & SUNBLOCK) | DRILLER & DRILLER’S OFFSIDER |
|  | LIFTING HEAVY EQUIPMENT | DO NOT LIFT OR MOVE HEAVY EQUIPMENT WITHOUT ASSISTANCE | DRILLER |
|  |  | USE PROPER BENDING / LIFTING TECHNIQUES BY LIFTING WITH ARMS AND LEGS AND NOT WITH BACK. KEEP BACK STRAIGHT WHILE LIFTING | DRILLER / OFF-SIDER |
|  |  | ALL WORK TO CEASE WHEN FUEL DELIVERING TANKER IS ON SITE. WORK CAN ONLY COMMENCE AFTER TANKER HAS LEFT SITE AND SITE IS AGAIN FREE OF EXPOLSIVE CONDITIONS | DRILLER / CONSULTANT |
|  |  | Use correct manual lifting methods. Wear correct PPE. | Driller’s offsider |
|  | MUSCLE STRAIN INJURY | STAND CLEAR OF ROTATING EQUIPMENT. NO LOOSE CLOTHING TO BE WORN. DRILLER TO MANAGE SAMPLING. | DRILLER / CONSULTANT |
|  | HANDLING CONTAMINATED MATERIALS / SOILS / GROUNDWATER | WORK UPWIND OF SAMPLING AREA IF POSSIBLE. | DRILLER / CONSULTANT |

# Text boxes

## Yes             No