|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 7/17/13 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Air Knifing Services |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Pre-construction Health & Safety Meeting/General Site Activities | See "General Site Activities" JSA | All employees assigned to this task will attend a pre-construction health and safety meeting, which will include the pertinent JSA, Site Safety Procedures, types of potential hazards, and actual hazards present and controls for those hazards. Show Hands. |  |
| Work zone delineation / Site setup | Traffic Hazards Fire/Explosion | Establish traffic control patterns as described in traffic control plan, utilizing cones, signage, and reflective traffic safety vests. Keep fire extinguisher within 25' of operation; Monitor area with PID or LEL meter to ensure vapor concentrations <10% LEL and below action level for contaminants of concern (see site-specific HASP for details). Smoking on site prohibited. |  |
| Asphalt / Concrete Cutting | Noise hazard from jack hammer Back injury from jack hammer or post hole diggers. Flying debris from jack hammer. Lacerations from saw cutting. | Only properly trained personnel are permitted to operate power equipment. Use proper hand and body positioning while using the saw and/or jackhammer. Use proper technique with post hole diggers. Wear safety glasses and hard hats ; Wear ear plugs to protect hearing. |  |
| Advance Air Knife Excavation | Flying debris from air lance. Minor/Major injury from pinch points Slips, trips, and falls | Wear PPE including face shields to protect eyes from debris and neck protection to protect throat/neck area Keep hands and clothing away from rotating machinery and discharge openings. Wear ear protection. Avoid contact with equipment and piping which may cause skin burns on contact. When operating, ensure adequate guards are in place on external moving parts. Check emergency shutoffs & whip checks. Keep equipment and tools in designated areas, maintain good housekeeping. |  |
| Backfill Excavation | Borehole Collapse Foot Injury Injury from stored energy | Ensure proper lifts of backfill are adequately compacted (consider using water to settle backfill). Most spoils should return in hole. Keep pneumatic tamper away from extremeties. Release pressure / vacuum from tanks. |  |
| Placement of drums | Back injury may occur. | Use drum cart/dolly if mechanical means not available; Use proper back injury prevention techniques when lifting or moving drums. Move drums by hand only when on solid ground. |  |
| Loading of Vehicle | Improper lifting techniques | Utilize proper lifting procedures when removing equipment and handling hoses. Bend at the knees and lift with the legs rather than the back. |  |
| 8. Depart from site | Traffic Hazards | Drive defensively and obey all traffic laws. Reduce speeds & signal intentions well in advance. |  |

# Text boxes

## Yes             No