|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: |  |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Concrete Saw Cutting |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| MOBILIZATION TO SITE | DRIVING ACCIDENTS | ALL VEHICLES TO COMPLY WITH CONNELLY DRIVING SAFETY STANDARDS | DRILLER / CONSULTANT |
|  |  | VEHICLE TO BE FIT FOR PURPOSE AND WELL MAINTAINED. | DRILLER / CONSULTANT |
|  |  | LOADS TO BE SECURE AND NOT TO EXCEED VEHICLE SPECIFICATIONS OR LEGAL LIMTS. | DRILLER / CONSULTANT |
|  |  | DRIVER TO BE LICENCED, TRAINED AND MEDICALLY FIT | DRILLER / CONSULTANT |
|  |  | DRIVER TO BE RESTED AND ALERT | DRILLER / CONSULTANT |
|  |  | MOBILE PHONE OR TWO-WAY RADIO TURNED OFF WHILE DRIVING | DRILLER / CONSULTANT |
|  |  | PLAN YOUR ROUTE AHEAD OF TIME - reference RM Journey Assessment | DRILLER / CONSULTANT |
|  |  | DRIVER NOT BE UNDER THE INFLUENCE OF ALCOHOL, DRUGS OR MEDICATION THAT IMPAIRS ABILITY TO DRIVE VEHICLE. | DRILLER / CONSULTANT |
| SET UP WORK SITE | AUTO / PUBLIC TRAFFIC | NOTIFY ATTENDANT OR SITE MANAGER / OWNER OF WORK ACTIVITIES AND LOCATION. |  |
|  |  | WORK LOCATION TO BE BARRICADED OFF; VEHICLE AND PEDISTRIAN TRAFFIC MANAGEMENT PLAN AS REQUIRED | DRILLER / Consultant |
| SET UP WORK SITE (Cont’d) | AUTO / PUBLIC TRAFFIC (Cont’d) | HIGH VISIBLE CLOTHING, STEEL CAP BOOTS, LONG SLEEVES/PANTS/ HARD HAT / SAFETY GLASSES TO BE WORN AT ALL TIMES WHILE IN OPERATIONAL AREAS | DRILLER / Consultant |
|  |  | INSPECT AREA AROUND VEHICLE PRIOR TO PUTTING VEHICLE IN MOTION AND USE SPOTTER | DRILLER / CONSULTANT |
|  | UNEVEN OR UNSTABLE GROUND | Visually examine site prior to entry. Place timbers under outriggers to spread load. | Driller |
|  | UNEVEN OR UNSTABLE GROUND | Visually examine site prior to entry. Place timbers under outriggers to spread load. | Driller |
|  |  | electrical spotter to be employed when working within 3 – 6.4 m (10 TO 20 FEET) of OHE lines; power company permit also required | CONSULTANT |
|  | UNDERGROUND SERVICES | UNDERGROUND SERVICES TO BE LOCATED PRIOR TO BREAKING GROUND BY QUALIFIED SERVICE LOCATOR | CONSULTANT / SERVICE LOCATOR / DRILLER |
| CONCRETE SAW CUTTING | IGNITION SOURCES / FIRE & EXPLOSION | ENSURE EQUIPMENT IS IN PROPER WORKING ORDER; INSPECT HANDLE, SAW BLADE, AND FRAMEWORK OF SAW | CONTRACTOR / DRILLER / CONSULTANT |
|  |  | APPLY WATER AS NECESSARY TO ADDRESS SURFACE SPARKING POTENTIAL | CONTRACTOR / DRILLER / CONSULTANT |
|  |  | AREA TO BE DEEMED FREE OF EXPOLSIVE CONDITIONS PRIOR TO WORK | CONSULTANT / DRILLER |
|  | HEARING DAMAGE DUE TO HIGH NOISE LEVELS | WEAR APPROPRIATE HEARING PROTECTION (EAR MUFFS OR EAR PLUGS) | CONTRACTOR / DRILLER / CONSULTANT |
|  |  | INSPECT ALL HAND TOOLS PRIOR TO USE. IF FAULTY OR INAPPROPRIATE, DO NOT USE UNTIL REPAIRED OR REPLACED | DRILLER |

# Text boxes

## Yes             No