|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 1/25/2013 |  | Job Number: | Clean Rivers/Cap Crossinging |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Drum Handling Using Lift Gate |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Arrive on site | Pedestrian traffic Slips/trips/falls Weather conditions | Use audio/visual warning devices (horn, beacon light, etc.) Identify safe area to work Wear appropriate PPE: Steel toe boots, leather work gloves, safety vest | Site Supervisor, Driver |
| Drop lift gate | Pinch points Crushing | One man completes task When second assist acknowledgement of task beginning must be used Ensure workers are clear of area before dropping gate | Driller |
| Enter truck and move drums onto gate | Pinch points Muscle strain | Two man task when handling full drum. Use communication on proper positioning when moving drum. | Driller, Helper |
| Lower drum and dispose empty contents | Pinch points Muscle strain | Rotate drum from lift gate to drum dolly when moving drum distance >10 ft. | Driver, Helper |

# Text boxes

## Yes             No