|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 5/23/13 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Hollow Stem Auger Method Drilling |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Who is responsible? Write the name of the person responsible (supervisor or above) to implement the control measure identified. |
| --- | --- | --- | --- |
| Pre-construction Health & Safety Meeting/General Site Activities | See "General Site Activities" JSA | All employees assigned to this task will attend a pre-drilling health and safety meeting, which will include the pertinent JSA, Site Safety Procedures, types of potential hazards, and actual hazards present and controls for those hazards. | All individuals on site. |
| Drill Rig Arrival and Set-Up. | Damage to Property or Equipment Roll Over Traffic Overhead and buried Utilities | Assess site and walk to boring locations. Determine the path of access and note any obstructions, uneven terrain, and soft ground that may impede access. Cross all hills and obstructions head on with masts lowered. Set riggers prior to raising mast. Utilize traffic control devices as outlined in traffic control program Position rig to avoid overhead lines by minimum distances specified in OSHA Regulation 29 CFR 1926.550. Use a spotter for overhead lines and other overhead obstructions; Underground utilities, piping, and other services must be marked out prior to excavation activities. (Ensure One-Call/Dig Safe service notified and cleared; conduct private utility locating for site services as practicable). Use vacuum excavation services to clear any questionable boring locations. | Driller and helper. |
| Drill Rig Inspection | Defective/damaged equipment | Inspection of equipment by qualified driller prior to use; replace or repair damaged items with manufacturer | Driller |
|  | Unapproved/Inappropriate hoisting equipment | Ensure all lifting hooks or attachments are self-closing; equipped with latches or pins; or are of other surrounding design (i.e. clevis hooks and screw pins) to prevent inadvertent release of objects being lifted | Driller |
|  | Damaged lifting devices/Non-specification lifting devices or materials | Inspect devices prior to each use; ensure all repairs or replacement parts meet minimum required tensile strength as specified by the equipment manufacturer. Ensure improper substitutes or damaged items are removed from service immediately. | Driller |
|  | Damaged Drive Assembly | Inspection of drive assembly by driller prior to use: cracks or damaged parts must be repaired or replaced. | Driller |
| Attach Auger Lengths | Back Strain | Use 2 people to lift and carry auger sections. Use mechanical lift devices whenever possible. | Driller and Helper |
|  | Crushed Foot | Steel toe shoes/boots | Driller and Helper |
|  | Pinched/Lacerated Fingers | Communication between employees when moving/attaching auger sections; Wear leather gloves when handling sections. Keep hands clear/out of pinch points. | Driller and Helper |
| Ground Intrusion Boring | Kick out | Clear the area of obstructions and communicate with all parties that drilling is beginning. Do not exceed manufacturers recommended rate of speed, force, torque, etc. Penetrate the ground slowly with hands on the controls for the first foot of soil. | Driller |
|  | Pinched Fingers/Caught in Rotation | Stay clear of rotating auger, never attempt to clean auger while in motion. Use long handled shovel to clear away cuttings when auger has stopped | Driller and Helper |
|  | Dust Exposure | Use safety glasses | Driller and Helper |
|  | Noise | Use hearing protection. | Driller and Helper |
|  | Overhead Falling Hazards | Use Hard Hat; remove overhead hazards promptly | Driller |
|  | Fire/Explosion | Keep fire extinguisher within 25' of operation; If No Smoking signs posted; smoking on site prohibited |  |
| Ground Intrusion: Split Spoon Sampling | Pinched/Lacerated fingers | Do not wrap rope around any part of the hand or body, maintain distance of at least 18 inches from in-running points. Eliminate excess rope, tie up loose clothing ; Wear leather gloves when handling materials or equipment | Driller and Helper |
|  | Slip/fall | Secure footing prior to operation; clear all trip hazards; clean/clear all slip hazards such as oils, ice, etc. ; keep materials/objects organized and out of walkways | Driller and Helper |
| Install Instrument Casing | Pinched/Lacerated fingers | Handle casing with care. Use mechanical locking devices to assist when possible. | Driller and Helper |
|  | Muscle strain/sprain | Two workers handling casing to alleviate stress/strain and potential muscle tearing. | Driller and Helper |
| Grout Boring Location | Dust inhalation | Wear mask to prevent overexposure to inhalation of grout particles. Or turn head opposite direction of wind when mixing grout. | Driller and Helper |
| Retrieve Augers | Pinched/Lacerated fingers | Helper is to wait for auger rotation to come to complete stop before removing soil from augers. At that time non verbal hand signals from Driller to Helper may instruct individual to begin removing auger. | Driller and Helper |

# Text boxes

## Yes             No