|  | Job Safety Analysis Worksheet |  |
| --- | --- | --- |

| Contractor: | Connelly & Associates, INC. |  | Date: | 6/5/13 |  | Job Number: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Team Name: |  |  |  |  | Job Name: |  |
| Team Leader: |  |  | JSA team members: | Name | Initials | Name | Initials |
| Description of work: | Operating loop reel |  |  |  |  |  |

| Activity List the tasks required to perform the activity in the sequence they are carried out. | Hazards Against each task list the hazards that could cause injury when the task is performed. | Risk control measures List the control measures required to eliminate or minimize the risk of injury arising from the identified hazard. | Exposure/Severity Ranking |
| --- | --- | --- | --- |
| Load 1.25” HDP loop with skid loader onto loop reel. Make sure loop real arms and pins are secured in place. | Pinch points Slips/trips/falls Moving loop real, causing crushing injury | With skid loader one person may load loop w/out skid loader, two person lift is required PPE: leather work gloves, steel toe boots |  |
| 2. Charging loop reel at job site. | whiplash from deteriorated hoses slips/trips/falls | Inspect hose before beginning work. Maintain proper footing and three points of contact when mounting/dismounting from trailer |  |
| 3. Dropping loop into drilled location. Two man involved activity. One man positioned at bobcat, maintaining eye contact with co-worker while controlling loop speed with hand brake. The other man positioned at drilled location maintaining control of loop. | Muscle strain/sprain Laceration injury Loss of control of loop could result in injury | Through communication the two man team will inform one another of possible “hang-ups” or “snags” that prevent loop from dropping in hole. Such problems like – belly on the loop or snag on loop when going down drilled location may occur. |  |
| 4. When dropping loop and facing the direction of the borehole. No worker should stand to the RIGHT SIDE of the loop reel. A busted bearing could cause a release of the loop and strike anyone standing in that vicinity. | Struck by/Crushing injury | Driller should remind crew and/or review JSA with new workers of correct area to stand while dropping loop. |  |
| 5. Cut loop using plastic pipe cutters. | Lacerations | Leather gloves and steel toe boots required. |  |

# Text boxes

## Yes             No